## Slide 1: Meep and MPB for waveguide simulations

## Slide 2: In this video
What is a waveguide?
Waveguide modes
  Very informal
Eigenmode solvers + demonstration with MPB
Waveguide modes in FDTD
  Eigenmode sources
  Eigenmode monitors
Demonstration of waveguide simulations in Meep
  Straight waveguide
  Waveguide bends

## Slide 3: Optical Waveguide
A wire for light

## Slide 4: Optical Waveguide
A wire for light
  Allows electromagnetic waves to travel in a confined space over long distances

## Slide 5: Optical Waveguide
A wire for light
Based on total internal reflection
cladding
cladding
core

## Slide 6: Optical Waveguide
A wire for light
Based on total internal reflection

## Slide 7: Optical Waveguide
A wire for light
Based on total internal reflection
Lossless propagation

## Slide 8: Optical Waveguide
A wire for light
Based on total internal reflection
Many different cross-sectional shapes, sizes, and materials
  Uniform along the propagation direction
https://www.intechopen.com/chapters/61838
Propagation direction

## Slide 9: Optical Waveguide
A wire for light
Based on total internal reflection
Many different cross-sectional shapes, sizes, and materials
Allows for photonic integrated circuits
Zhang, G., Haw, J.Y., Cai, H. et al. An integrated silicon photonic chip platform for continuous-variable quantum key distribution. Nat. Photonics 13, 839–842 (2019). https://doi.org/10.1038/s41566-019-0504-5

## Slide 10: Optical Waveguide
A wire for light
Based on total internal reflection
Many different cross-sectional shapes, sizes, and materials
Allows for photonic integrated circuits
  Optical communications
  Photonic computing
  Quantum optics
  etc.
Zhang, G., Haw, J.Y., Cai, H. et al. An integrated silicon photonic chip platform for continuous-variable quantum key distribution. Nat. Photonics 13, 839–842 (2019). https://doi.org/10.1038/s41566-019-0504-5

## Slide 11: Electric Field in Waveguide
Waveguide is uniform along the propagation direction (y)

## Slide 12: Electric Field in Waveguide
Waveguide is uniform along the propagation direction ()

## Slide 13: Electric Field in Waveguide
Waveguide is uniform along the propagation direction ()

## Slide 14: Electric Field in Waveguide
Effective wavenumber
Effective wavelength

## Slide 15: Electric Field in Waveguide
Effective wavenumber
Effective wavelength
Vacuum wavelength
Effective refractive index

## Slide 16: Electric Field in Waveguide
more generally …

## Slide 17: Electric Field in Waveguide
more generally …

## Slide 18: Electric Field in Waveguide
Plug this into Maxwell’s equations
+ algebra and calculus

## Slide 19: Electric Field in Waveguide
Plug this into Maxwell’s equations
+ algebra and calculus
Differential operator
scalar value

## Slide 20: Electric Field in Waveguide
Plug this into Maxwell’s equations
+ algebra and calculus
Differential operator
Eigenvalue problem!

## Slide 21: Electric Field in Waveguide
Plug this into Maxwell’s equations
+ algebra and calculus
Differential operator
Eigenvalue problem!
Effective wavenumber = Eigenvalue

## Slide 22: Electric Field in Waveguide
Eigenvalue Equation
Eigenmode solutions
In general, there are multiple solutions = Waveguide modes

## Slide 23: Eigenmode Solvers
Finds waveguide modes for arbitrary waveguide shapes and electromagnetic frequencies
https://www.intechopen.com/chapters/61838

## Slide 24: Eigenmode Solvers
Finds waveguide modes for arbitrary waveguide shapes and electromagnetic frequencies
Use only cross-section of the waveguide
z
x
y

## Slide 25: Eigenmode Solvers
Finds waveguide modes for arbitrary waveguide shapes and electromagnetic frequencies
Use only cross-section of the waveguide
Returns:
  Mode EM field profiles
  Effective wavenumbers
  Effective refractive index

## Slide 26: Eigenmode Solvers
z
x
y

## Slide 27: Eigenmode Solvers
Waveguide cross-section
z
x
z
x
y

## Slide 28: Eigenmode Solvers
z
x
z
x
y
Returns mode fields and wavenumber
Waveguide cross-section

## Slide 29: Code break
Use MPB to calculate and visualize the waveguide mode for a buried Silicon-on-insulator waveguide
SiO2
Si

## Slide 30: Waveguide modes in FDTD
Eigenmode source
  source for waveguide simulations
Eigenmode expansion monitor
  monitors for waveguide simulations
z
x
y

## Slide 31: Waveguide modes in FDTD
Eigenmode source
  Source for waveguide simulations
  User choses (mode index and frequency)
z
x
y

## Slide 32: Waveguide modes in FDTD
Eigenmode source
  User choses (mode index and frequency)
  Chose source-plane location and direction
z
x
y

## Slide 33: Waveguide modes in FDTD
Eigenmode source
  User choses (mode index and frequency)
  Chose source-plane location and direction
  Eigenmode solver calculates
z
x
y

## Slide 34: Waveguide modes in FDTD
Eigenmode source
  User choses (mode index and frequency)
  Chose source-plane location and direction
  Eigenmode solver calculates
  Inject and using a pulse-source
z
x
y

## Slide 35: Waveguide modes in FDTD
Eigenmode expansion monitor
  Monitor for waveguide simulations
  Calculates overlap integral of with
z
x
y

## Slide 36: Waveguide modes in FDTD
Eigenmode expansion monitor
z
x
y
Mode overlap integral
Mode amplitude

## Slide 37: Waveguide modes in FDTD
Eigenmode expansion monitor
z
x
y
Mode overlap integral
Mode amplitude is directional – can distinguish between backwards (-) and forward (+) travelling fields

## Slide 38: Waveguide modes in FDTD
Eigenmode expansion monitor
  Power carried by mode in direction:
Mode overlap integral
z
x
y

## Slide 39: Waveguide modes in FDTD
Eigenmode expansion monitor
  Power carried by mode in direction:
  Transmittance/Reflectance spectra
Forward mode amplitude in front of source

## Slide 40: Waveguide modes in FDTD
Eigenmode expansion monitor
  Power carried by mode in direction:
  Transmittance/Reflectance spectra
Forward mode amplitude in front of source
Forward mode amplitude at

## Slide 41: Waveguide modes in FDTD
Eigenmode expansion monitor
  Power carried by mode in direction:
  Transmittance/Reflectance spectra
Forward mode amplitude in front of source
Forward mode amplitude at
Backward mode amplitude a

## Slide 42: Code break
Use Meep to simulate light propagating through a buried waveguide
Plot reflectance and transmittance

## Slide 43
z
x
y